## Slide 1
Electrical
Notes: This presentation is designed to assist trainers conducting OSHA 10-hour General Industry outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of 1970 or for any standards issued by the U.S. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the U.S. Department of Labor.

## Slide 2: Introduction
An average of one worker is electrocuted on the job every day
There are four main types of electrical injuries:
  Electrocution (death due to electrical shock)
  Electrical shock
  Burns
  Falls
Notes: This module addresses OSHA’s General Industry electrical standards contained in 29 CFR 1910 Subpart S. OSHA also has electrical standards for construction and maritime, but recommends that employers in these industries follow the general industry electrical standards whenever possible for hazards that are not addressed by their industry-specific standards.
Suitability of electrical equipment for an identified purpose may be evidenced by listing or labeling by a nationally recognized testing laboratory which makes periodic inspections of equipment production and states that such equipment meets nationally recognized standards or tests to determine safe use in a specified manner.
The Lockout/Tagout (LOTO) standard, 29 CFR 1910.147, is not covered in this presentation. However, you can find information on the Lockout-Tagout Interactive Training Program, under “OSHA Advisors” on the OSHA web site, www.osha.gov.
Electricity is one of the most common causes of fire in homes and workplaces. Explosions have also resulted from electrical sources.

## Slide 3: Electrical Terminology
Current – the movement of electrical charge
Resistance – opposition to current flow
Voltage – a measure of electrical force
Conductors – substances, such as metals, that have little resistance to electricity
Insulators – substances, such as wood, rubber, glass, and bakelite, that have high resistance to electricity
Grounding – a conductive connection to the earth which acts as a protective measure
Notes: Operating an electric switch is like turning on a water faucet. Behind the faucet or switch there must be a source of water or electricity with something to transport it, and with a force to make it flow. In the case of water, the source is a reservoir or pumping station; the transportation is through pipes; and the force to make it flow is provided by a pump. For electricity, the source is the power generating station; current travels through electric conductors (wires); and the force to make it flow - voltage, measured in volts, is provided by a generator.
Resistance
- Dry skin has a fairly high resistance, but when moist, resistance drops radically, making it a ready conductor.
- Measured in ohms.
Use extra caution when working with electricity when water is present in the environment or on the skin. Pure water is a poor conductor, but small amounts of impurities, such as salt and acid (both are contained in perspiration), make it a ready conductor.

## Slide 4: Electrical Shock
Received when current passes through the body
Severity of the shock depends on:
  Path of current through the body
  Amount of current flowing through the body
  Length of time the body is in the circuit
LOW VOLTAGE DOES NOT MEAN LOW HAZARD
Notes: A small current that passes through the trunk of the body (heart and lungs) is capable of causing severe injury or electrocution.
Low voltages can be extremely dangerous because, all other factors being equal, the degree of injury increases the longer the body is in contact with the circuit.

## Slide 5: Dangers of Electrical Shock
Currents greater than 75 mA* can cause ventricular fibrillation (rapid, ineffective heartbeat)
Will cause death in a few minutes unless a defibrillator is used
75 mA is not much current – a small power drill uses 30 times as much
* mA = milliampere = 1/1,000 of an ampere
Defibrillator in use

## Slide 6: How is an electrical shock received?
When two wires have different potential differences (voltages), current will flow if they are connected together
  In most household wiring, the black wires are at 110 volts relative to ground
  The white wires are at zero volts because they are connected to ground
If you come into contact with an energized (live) black wire, and you are also in contact with the white grounded wire, current will pass through your body and YOU WILL RECEIVE A SHOCK
Notes: Grounding is a physical connection to the earth, which is at zero volts.
Electricity travels in closed circuits, and its normal route is through a conductor. Electric shock occurs when the body becomes a part of the circuit. Electric shock normally occurs in one of three ways - when an individual is in contact with the ground and contacts:
1. Both wires of an electric circuit, or
2. One wire of an energized circuit and the ground, or
3. A metallic part that has become energized by contact with an energized conductor. The metal parts of electric tools and machines may become energized if there is a break in the insulation of the tool or machine wiring. A worker using these tools and machines is made less vulnerable to electric shock when there is a low-resistance path from the metallic case of the tool or machine to the ground. This is done through the use of an equipment grounding conductor—a low-resistance wire that causes the unwanted current to pass directly to the ground, thereby greatly reducing the amount of current passing through the body of the person in contact with the tool or machine.

## Slide 7: How is an electrical shock received? (cont’d)
If you are in contact with an energized wire or any energized electrical component, and also with any grounded object, YOU WILL RECEIVE A SHOCK
You can even receive a shock when you are not in contact with a ground
  If you contact both wires of a 240-volt cable, YOU WILL RECEIVE A SHOCK and possibly be electrocuted
Notes: Contact with both energized wires of a 240-volt cable will deliver a shock. This type of shock can occur because one live wire may be at +120 volts while the other is at –120 volts during an alternating current cycle, which is a potential difference of 240 volts.

## Slide 8: Electrical Burns
Most common shock-related, nonfatal injury
Occurs when you touch electrical wiring or equipment that is improperly used or maintained
Typically occurs on the hands
Very serious injury that needs immediate attention

## Slide 9: Falls
Electric shock can also cause indirect or secondary injuries
Workers in elevated locations who experience a shock can fall, resulting in serious injury or death

## Slide 10: Inadequate Wiring Hazards
A hazard exists when a conductor is too small to safely carry the current
Example: using a portable tool with an extension cord that has a wire too small for the tool
  The tool will draw more current than the cord can handle, causing overheating and a possible fire without tripping the circuit breaker
  The circuit breaker could be the right size for the circuit but not for the smaller-wire extension cord
Wire Gauge
WIRE
Wire gauge measures wires ranging in size from number 36 to 0 American wire gauge (AWG)
Notes: Note that wire-gauge size is inversely related to the diameter of the wire. For example, a No. 12 flexible cord has a larger diameter wire than a No. 14 flexible cord.

## Slide 11: Overload Hazards
If too many devices are plugged into a circuit, the current will heat the wires to a very high temperature, which may cause a fire
If the wire insulation melts, arcing may occur and cause a fire in the area where the overload exists, even inside a wall
Notes: If the circuit breakers or fuses are too big (high current rating) for the wires they are supposed to protect, an overload in the circuit will not be detected and the current will not be shut off. A circuit with improper overcurrent protection devices – or one with no overcurrent protection devices at all – is a hazard.

## Slide 12: Electrical Protective Devices
These devices shut off electricity flow in the event of an overload or ground-fault in the circuit
Include fuses, circuit breakers, and ground-fault circuit-interrupters (GFCI’s)
Fuses and circuit breakers are overcurrent devices
  When there is too much current:
    Fuses melt
    Circuit breakers trip open
Notes: The basic idea of an overcurrent device is to make a weak link in the circuit. In the case of a fuse, the fuse is destroyed before another part of the system is destroyed. In the case of a circuit breaker, a set of contacts opens the circuit. Unlike a fuse, a circuit breaker can be re-used by re-closing the contacts. Fuses and circuit breakers are designed to protect equipment and facilities, and in so doing, they also provide considerable protection against shock in most situations. However, the only electrical protective device whose sole purpose is to protect people is the ground-fault circuit-interrupter.

## Slide 13: Ground-Fault Circuit Interrupter
This device protects you from dangerous shock
The GFCI detects a difference in current between the black and white circuit wires
(This could happen when electrical equipment is not working correctly, causing current “leakage” – known as a ground fault.)
If a ground fault is detected, the GFCI can shut off electricity flow in as little as 1/40 of a second, protecting you from a dangerous shock
Notes: The GFCI continually matches the amount of current going to an electrical device against the amount of current returning from the device along the electrical path.
Whenever the amount of current going differs from the amount returning by approximately 5 milliamperes, the GFCI interrupts the electric power within as little as 1/40 of a second, protecting you from a dangerous shock.
GFCI’s are able to detect the loss of current resulting from leakage through a person who is beginning to be shocked. If this situation occurs, the GFCI switches off the current in the circuit.
GFCI’s are different from circuit breakers and fuses because they detect leakage currents rather than overloads.

## Slide 14: Grounding Hazards
Some of the most frequently violated OSHA standards
Metal parts of an electrical wiring system that we touch (switch plates, ceiling light fixtures, conduit, etc.) should be at zero volts relative to ground
Housings of motors, appliances or tools that are plugged into improperly grounded circuits may become energized
If you come into contact with an improperly grounded electrical device, YOU WILL BE SHOCKED
Notes: Grounding is a physical connection to the earth, which is at zero volts.
Current flows through a conductor if there is a difference in voltage (electrical force). If metal parts of an electrical wiring system are at zero volts relative to ground, no current will flow if our body completes the circuit between these parts and ground.
Two kinds of grounds are required by the standard:
1. Service or system ground. In this instance, one wire — called the neutral conductor or grounded conductor — is grounded. In an ordinary low-voltage circuit, the white (or gray) wire is grounded at the generator or transformer and again at the service entrance of the building. This type of ground is primarily designed to protect machines, tools, and insulation against damage.
2. For enhanced worker protection, an additional ground, called the equipment ground, must be furnished by providing another path from the tool or machine through which the current can flow to the ground. This additional ground safeguards the electric equipment operator if a malfunction causes the metal frame of the tool to become energized.

## Slide 15: Overhead Powerline Hazards
Most people don’t realize that overhead powerlines are usually not insulated
Powerline workers need special training and personal protective equipment (PPE) to work safely
Do not use metal ladders – instead, use fiberglass ladders
Beware of powerlines when you work with ladders and scaffolding
Notes: Overhead power lines must be deenergized and grounded by the owner or operator of the lines, or other protective measures must be provided before work is started. Protective measures (such as guarding or insulating the lines) must be designed to prevent contact with the lines.
Minimum clearance distances for employees working in the vicinity of overhead power lines are given in 29 CFR 1910.333(c)(3).
PPE may consist of rubber insulating gloves, hoods, sleeves, matting, blankets, line hose, and industrial protective helmets.

## Slide 16
Some Examples of OSHA Electrical Requirements . . . .
Notes: Electrical accidents appear to be caused by a combination of three factors:
1. Unsafe equipment and/or installation,
2. Workplaces made unsafe by the environment, and
3. Unsafe work practices.
There are various ways of protecting people from the hazards caused by electricity. These include: insulation, guarding, grounding, electrical protective devices, and safe work practices.

## Slide 17: Grounding Path
The path to ground from circuits, equipment, and enclosures must be permanent and continuous
Violation shown here is an extension cord with a missing grounding prong
Notes: 1910.304(f)(4)

## Slide 18: Hand-Held Electric Tools
Hand-held electric tools pose a potential danger because they make continuous good contact with the hand
To protect you from shock, burns, and electrocution, tools must:
  Have a three-wire cord with ground and be plugged into a grounded receptacle, or
  Be double insulated, or
  Be powered by a low-voltage isolation transformer
Notes: 1910.304(f)(5)(v)(C)(3)
Hazards of portable electric tools:
Currents as small as 10 mA can paralyze, or “freeze” muscles
- Person cannot release tool
- Tool is held even more tightly, resulting in longer exposure to shocking current
Power drills use 30 times as much current as what will kill.
Double-insulated equipment must be distinctly marked to indicate that the equipment utilizes an approved system of double insulation. The common marking is:

## Slide 19: Guarding of Live Parts
Must guard live parts of electric equipment operating at 50 volts or more against accidental contact by:
  Approved cabinets/enclosures, or
  Location or permanent partitions making them accessible only to qualified persons, or
  Elevation of 8 ft. or more above the floor or working surface
Mark entrances to guarded locations with conspicuous warning signs
Notes: 1910.303(g)(2)(i)
1910.303(g)(2)(iii)

## Slide 20: Guarding of Live Parts
Must enclose or guard electric equipment in locations where it would be exposed to physical damage
Violation shown here is physical damage to conduit
Notes: 1910.303(g)(2)(ii)

## Slide 21: Cabinets, Boxes, and Fittings
Junction boxes, pull boxes and fittings must have approved covers
Unused openings in cabinets, boxes and fittings must be closed (no missing knockouts)
Photo shows violations of these two requirements
Notes: 1910.305(b)(1) and (2)

## Slide 22
Use of Flexible Cords
More vulnerable than fixed wiring
Do not use if one of the recognized wiring methods can be used instead
Flexible cords can be damaged by:
  Aging
  Door or window edges
  Staples or fastenings
  Abrasion from adjacent materials
  Activities in the area
Improper use of flexible cords can cause shocks, burns or fire
Notes: 1910.305(g)

## Slide 23: Permissible Uses of Flexible Cords Examples
Pendant, or
Fixture Wiring
Portable lamps,
tools or appliances
Stationary equipment-to facilitate interchange
Notes: 1910.305(g)(1)(i)
Other examples:
Elevator cables
Wiring of cranes and hoists
Prevention of the transmission of noise or vibration
Appliances where the fastening means and mechanical connections are designed to permit removal for maintenance and repair
Data processing cables approved as part of the data processing system

## Slide 24: Prohibited Uses of Flexible Cords Examples
Substitute for fixed wiring
Run through walls, ceilings, floors, doors, or windows
Concealed behind or attached to building surfaces
Notes: 1910.305(g)(1)(iii)

## Slide 25: Clues that Electrical Hazards Exist
Tripped circuit breakers or blown fuses
Warm tools, wires, cords, connections, or junction boxes
GFCI that shuts off a circuit
Worn or frayed insulation around wire or connection

## Slide 26: Training
Deenergizing electric equipment before inspecting or making repairs
Using electric tools that are in good repair
Using good judgment when working near energized lines
Using appropriate protective equipment
Train employees working with electric equipment in safe work practices, including:
Notes: OSHA’s electrical safety-related work practice requirements are contained in 29 CFR 1910.331-.335.
Deenergizing Electrical Equipment. The accidental or unexpected sudden starting of electrical equipment can cause severe injury or death. Before ANY inspections or repairs are made the current must be turned off at the switch box and the switch padlocked in the OFF position. At the same time, the switch or controls of the machine or other equipment being locked out of service must be securely tagged to show which equipment or circuits are being worked on.
For more information on the Lockout/Tagout (LOTO) standard, 1910.147, see the Lockout/Tagout Interactive Training Program at the osha web site, www.osha.gov and find this reference under “OSHA Advisors”.

## Slide 27: Summary
Hazards
Inadequate wiring
Exposed electrical parts
Wires with bad insulation
Ungrounded electrical systems and tools
Overloaded circuits
Damaged power tools and equipment
Using the wrong PPE and tools
Overhead powerlines
All hazards are made worse in wet conditions
Protective Measures
Proper grounding
Using GFCI’s
Using fuses and circuit breakers
Guarding live parts
Proper use of flexible cords
Training